## Slide 1
INTRO TO CYS
SEMESTER PROJECT
GROUP MEMBERS:
Bilad Ul Haq 242340
M. Raess ul Abedian 242354
Muhammad Bilal 242372
Sana Sadiq 242374

## Slide 2
VULNERABILITY IN THE 4-WAY HANDSHAKE:
  During the 4-way handshake process in WPA/WPA2, encrypted authentication data (PMKID) is exchanged between the client and access point.
  Attackers can capture this handshake data and perform offline dictionary or brute-force attacks to crack the network password.
Deauthentication Frames:
  WPA/WPA2 networks accept unauthenticated deauthentication frames sent by any device, without verifying their legitimacy.
  This allows attackers to perform deauthentication attacks, forcibly disconnecting users from the network.

## Slide 3
VULNERABILITY IN THE 4-WAY HANDSHAKE:
Weak Password Practices:
  Many networks rely on weak or common passwords, making them highly susceptible to dictionary attacks.
  Once the attacker captures the handshake, weak passwords can be cracked in minutes using tools like Hashcat.
Lack of Protection Against Mass Deauthentication:
  WPA/WPA2 does not inherently protect against mass deauthentication attacks, allowing attackers to repeatedly disrupt network connectivity.

## Slide 4
DETAILED EXPLOITATION OF THE VULNERABILITY:
Initial Setup
Scanning for Target Networks:
  Set the wireless network interface to monitor mode using tools like airmon-ng
  Monitor mode allows capturing all wireless traffic in the vicinity, including management frames and handshake packets.
Configuring Wireless Interface:
  Use tools like Airgeddon to scan nearby wireless networks.
  Identify the target access point (AP) based on its SSID and BSSID (MAC address).

## Slide 5
DETAILED EXPLOITATION OF THE VULNERABILITY:
Execution
Capturing the WPA Handshake:
  Launch a deauthentication attack to force connected clients to disconnect from the network.
  This attack leverages unprotected management frames to send "deauth" commands to devices.
Deauthentication Attack:
  When legitimate clients reconnect, capture the WPA handshake exchanged between the client and the AP.
  The handshake file contains encrypted authentication data that can be brute-forced offline.

## Slide 6
DETAILED EXPLOITATION OF THE VULNERABILITY:
Execution
  Use a dictionary or wordlist to try various passwords against the captured handshake using tools like Hashcat or Aircrack-ng.
  Success depends on the strength and complexity of the network password.
Performing a Dictionary Attack:

## Slide 7
04
DETAILS ABOUT THE TOOLS USED TO EXPLOIT THE VULNERABILITY:
Tool: Airgeddon
Overview:
  Airgeddon is a powerful wireless network security auditing framework designed for penetration testing.
  It automates various wireless attack techniques and integrates multiple tools into one cohesive platform
  The latest version (e.g., 11.20 or newer) is highly versatile, supporting WPA/WPA2 auditing and other advanced attacks.
Platform Requirements:
  Runs on Kali Linux or any Debian-based Linux distribution.
  Requires root access to execute network operations effectively.

## Slide 8
04
DETAILS ABOUT THE TOOLS USED TO EXPLOIT THE VULNERABILITY:
Tool: Airgeddon
Hardware Requirements:
  Requires a wireless network adapter capable of:
  Monitor Mode: Captures raw network traffic.
  Packet Injection: Sends malicious packets for deauthentication or Evil Twin attacks.
  Examples of compatible adapters:
Alfa AWUS036NHA
TP-Link TL-WN722N (v1)

## Slide 9
04
DETAILS ABOUT THE TOOLS USED TO EXPLOIT THE VULNERABILITY:
Tool: Airgeddon
Capabilities:
Combines multiple wireless attack techniques, including:
  Deauthentication Attacks: Forcibly disconnect clients to capture handshake data.
  Handshaking and Cracking: Captures WPA/WPA2 handshake for offline password cracking.
  Evil Twin Attack: Creates a rogue access point to deceive users.
  DoS (Denial of Service): Disrupts network connectivity temporarily.
  Integrates tools like Aircrack-ng, Hashcat, and others for exploitation.

## Slide 10
HOW TO PATCH THE VULNERABILITY:
Upgrade to
WPA3:
  Use WPA3, which offers enhanced protection by replacing the 4-way handshake with Simultaneous Authentication of Equals (SAE), making it resistant to offline dictionary attacks.
Strengthen Password Practices:
  Ensure passwords are long, complex, and unique, making brute-force or dictionary attacks infeasible.
Implement WPA Enterprise:
  In corporate environments, use WPA Enterprise with RADIUS servers for centralized authentication, adding an extra layer of security..
Update Firmware and Security Protocols:
  Regularly update router firmware to patch known vulnerabilities.
  Ensure the latest WPA/WPA2 security standards are applied.

## Slide 11
10
THANK YOU